## Slide 1
Woodturning
The wood lathe produces round project parts.

## Slide 2: SPINDLE TURNING = “TURNING BETWEEN CENTERS” = SPUR DRIVE IN HEADSTOCK AND CENTER IN TAILSTOCK

## Slide 3
Small Spur Center
Large Spur Center
Live Center
Dead Center
Spindles are held between a spur center and live or dead center.
Live Center

## Slide 4: Cut two kerfs in the wood crossing in the center to fit on the spur drive.
Spur Drive

## Slide 5: Cut the kerfs with a handsaw OR a V-Block and the bandsaw.

## Slide 6: Place the wood on a solid table or floor. NEVER pound on the wood in or on the lathe.

## Slide 7: Never use a hard metal hammer. It will “marshmallow” the end of the spur drive.

## Slide 8: Use a wooden mallet.

## Slide 10: Place the spur drive with the wood in the headstock.

## Slide 11: Hold the other end with a center in the tailstock.

## Slide 12: Check that the groove lines up with the bolt.
Front Side
Back Side

## Slide 14: 1. Check for end-to-end play. 2. Rotate the wood by hand to make sure it doesn’t hit the tool rest.

## Slide 15: Start on SLOW SPEED. Speed is controlled with a dial and with pulleys and belts.

## Slide 17: ABC’s of Lathe Turning

## Slide 18: A = Anchor the Tool on the Tool Rest.

## Slide 19: A = Anchor Your Hand on the Tool Rest too. Like this…

## Slide 20: Like this…

## Slide 21: or like this.

## Slide 22: Like this.

## Slide 23: B = Bevel.

## Slide 24: B = Bevel. Touch the wood with the BEVEL first.

## Slide 25: This tool is a roughing gouge. You always tilt it upward.

## Slide 26: C = Cut. Gradually raise the handle and lower the cutting edge into the wood until it begins to cut.

## Slide 27
To get the proper leverage, keep the tool rest close to the work.
The steep angle of the tool is a shear cut which is more efficient.
With the tool rest close, the tool is easier to control.

## Slide 28
If the tool rest is too far from the work, the tool is hard to control.
A scraping cut is less efficient and puts more stress on the work.

## Slide 29
Not to mention the fact that leverage that favors the machine over the operator can rip a tool from your grasp.

## Slide 30
Think Safety
Wear a face shield.
Make sure everything is properly tightened.
Anchor the tool & your hand on the tool rest.
Use mostly lower speeds.
Keep the tool rest 1/8” from the project.
Keep the tools sharp.
Remove the tool rest before sanding.

## Slide 31: Use the knockout bar to tap on and loosen the spur drive

## Slide 32: Keep your hand on the spur drive to catch it so it doesn’t fly out and land on the hard floor.

## Slide 33: Clean out any sawdust or grit from inside the head stock with the green squeegy.

## Slide 34: Grit will cause pits, grooves and burrs preventing the spur drive from seating properly and also make it difficult to remove the spur drive.