## Slide 1: Delta Scroll Saw

## Slide 2: Changing Blades

## Slide 3: FIRST RELEASE THE TENSION BY MOVING THE TENSIONING LEVER FORWARD

## Slide 4: Release Tension—move lever forward.

## Slide 6: Handle of Hex Wrench to Loosen Blade Locking Screw

## Slide 7: Hex Wrench

## Slide 8: Tool to keep blade clamp from twisting while loosening screw

## Slide 9: Use both tools to loosen clamp.

## Slide 11: Loosen the bottom clamp with both tools the same as at the top.

## Slide 12: Removing this circular plate makes it easier to position the blade in the clamps.

## Slide 13: Don’t forget, the teeth point down.

## Slide 14: After installing the new blade, apply tension by moving the lever back to its original position.

## Slide 16: If the blade is too loose or too tight, release the lever, turn this knob, and tighten the lever again.

## Slide 17: When plucked, the blade should ring with a high clear note.

## Slide 18: Guide (V-shape) goes directly behind, but not rubbing on blade.

## Slide 20: Pressure foot sits directly on wood to keep wood from bouncing up and down with the blade.

## Slide 22: On/Off and Variable Speed Control

## Slide 23: MAKING INSIDE CUTS—Drill a hole insert the blade through the hole.

## Slide 24: Excalibur Scroll Saw Tensioning Lever

## Slide 26: Pressure foot on Excalibur Scroll Saw.

## Slide 27: Adjusting the height of the pressure foot.

## Slide 28: Knob to make small adjustments to tension.

## Slide 29: Adjust tension here.

## Slide 30: On/Off Switch

## Slide 31: Set speed On/Off Switch

## Slide 32: Plastic tube blows sawdust away so you can see where you are cutting.